2-Year Earth-to-Earth Trajectory

ASEN 5519

Computing the ’s for the Earth-to-Earth portion of the VEEGA trajectory is one of the trickier parts of the final project.  At Venus, we can use Lambert’s problem to compute the  and .  We can compute the  for the first EGA and  for the second EGA using Lambert’s problem as well.  However, we can not use Lambert’s problem to compute the  for the first EGA or  for the second EGA.  The only constraint that we have is that the spacecraft must return to the same position two years later (since we already know that Earth will essentially return to the same place in two years).  Using this information, it is straightforward to compute the magnitude of the sun-centered velocity vector immediately following the first EGA, as follows:

However, in order to compute the appropriate B-plane parameters, we need to know the vector components of the velocity.  Figure 1 shows the geometry of the velocity vector immediately after the first EGA.  This diagram shows that there are infinitely many possibilities that would place the spacecraft into a 2-year orbit, all of which lie on the illustrated circle.

Figure 1: Diagram illustrating the possible orientations of the spacecraft velocity vector immediately after the first EGA.

Using the law of cosines, the angle  can be computed.

where,

Now we can compute the outgoing hyperbolic excess velocity vector () as a function of  and .

This vector is expressed in a coordinate system in which the x-axis lies along the Earth’s velocity vector (as can be seen from figure 1).  We’ll call this reference frame “frame 1”.  The Earth’s velocity vector is not necessarily along the x-axis of the ecliptic frame, thus  needs to be rotated from frame 1 into the ecliptic coordinate frame.  First, we assume that the Earth’s velocity vector lies in the ecliptic x-y plane.  Figure 2 shows the geometry of the Earth’s velocity vector and the outgoing hyperbolic excess velocity vector in the ecliptic reference frame.  Note that Earth’s velocity vector is in the x-y frame, however the outgoing hyperbolic excess velocity vector is not.

Figure 2:  Diagram illustrating the geometry of the Earth’s velocity vector and the outgoing hyperbolic excess velocity vector in the ecliptic reference frame.

From figure 2, we can see that the rotation from frame 1 to the ecliptic frame is simply a rotation of  about the z-axis.

where  and

# Algorithm

Given: ,  for EGA 1

Compute P, a, E, and

Compute  using:

Compute

Compute

Loop over 0 <  < 2*pi

Compute

Compute

Use  to make sure EGA 1 and EGA 2 do not go below the surface of Earth

If both EGAs work, save the vector.

End loop

# Text boxes



xecliptic

zecliptic

V(





Locus of 2-Year Orbits

VEarth

Vsc_sun

V(

VEarth

yecliptic